## Slide 1
Introduction in Performance Modeling
Performance Evaluation of the Internet of Things (IoT)
Module Course: Performance Evaluation of Distributed Systems
Prof. Tobias Hoßfeld, Summer Semester 2022
Chapter 1

## Slide 2: Disclaimer and Copyright Notice
Lecture slides, figures, and scripts are based on the open access text book “Performance Modeling and Analysis of Communication Networks”. The book and scripts are licensed under the Creative Commons License Attribution-ShareAlike 4.0 International (CC BY-SA 4.0). If you remix, transform, or build upon the material, you must distribute your contributions under the same license as the original.
The book must be cited and the disclaimer attached when using lectures slides or scripts.
Tran-Gia, P. & Hossfeld, T. (2021). Performance Modeling and Analysis of Communication Networks - A Lecture Note. Würzburg University Press. https://doi.org/10.25972/WUP-978-3-95826-153-2
Website to download book, exercises, slides and scripts: https://modeling.systems/

## Slide 3: Chapter 1
1 Introduction in Performance Modeling
1.1 Modeling Concept and Levels of Abstraction
1.2 Notation for Single-Stage Queueing Models
1.2.1 Kendall’s Notation
1.2.2 Extended Kendall’s Notation: A/B/n/S/m/D
1.3 Modeling Examples
    1.3.1 Handshaking Protocol
    1.3.2 Network Dimensioning in Mobile Networks
    1.3.3 Software Defined Networking and Switch Table Occupancy
    1.3.4 Video Streaming Applications and QoE
    1.3.5 Resource Sharing in Cloud Computing
    1.3.6 Internet of Things and Smart City Applications
    1.3.7 Overload Control in Communication Systems

## Slide 4: Example: Internet of Things (IoT)
Some relevant questions
  How can an IoT system with millions of sensors be modeled? What is the scalability of such a system?
  How many gateways are needed in a smart city to ensure good quality of service?
  How can server capacity be dimensioned in a cloud? How many servers or VMs are required?
  How well does channel access mechanism work for technologies such as nB-IoT or LoRaWAN? What is the probability of a successful data transfer? What is the energy efficiency of the channel access?
Models from queuing theory applied to IoT systems

## Slide 5: IoT System
Things networked using Internet technologies
  may be resource constrained (energy consumption, RAM, ROM)
  may have to sent a couple of bytes only
Smart Things
IoT Gateways
Online Services
Internet

## Slide 6: IoT Gateway
Bridges the communication gap between IoT devices and the cloud, e.g. translating protocols, adding security features, etc.
May offer local processing, filtering, caching, storage solutions
May control smart things
Advantages: lowering costs, mitigate risks, operation and management
Smart Things
IoT Gateways
Online Services
Internet

## Slide 7: Example: IoT Cloud
How to dimension an IoT cloud load balancer? How much traffic from IoT sensors can be handled such that average waiting time is below a treshold? What is the required processing power?
Arrival process
Arrival times
Waiting
space
Service
unit
Departure
times
Processing
time
Waiting
time

## Slide 9: Example: LoRaWAN
LoRaWAN Slave
LoRaWAN Master
Customer Application
Customer Application/ Server Logic
LoRa PHY: Modulation
LoRa PHY
PHY
MAC
Backhaul IP Stack
PHY
MAC
Backhaul IP Stack
Packet Forwarding
sensor
gateway
network server
encrypted
encrypted
LoRa
Ethernet, 3G, WiFi
What is the performance and energy efficiency of LoRaWAN‘s channel access?
LoRa MAC
LoRa MAC

## Slide 10: Example: LoRaWAN (f.)
What are the system components?
Arrival process
Arrival times
Waiting
space
Service
unit
Departure
times
Processing
time
Waiting
time

## Slide 11: Example: Video Streaming
What is the Quality of Experience of HTTP-based video streaming?
Cloud / DC
Access Network
Core Network
Access Network
Cloud / DC
IP
IP
IP
IP

## Slide 12: Modeling Concepts
Level of abstraction

## Slide 13: Abstraction Layering of Performance Analysis Techniques

## Slide 14: Modeling
(formal) model
real system
goal: real-world solution & answer
(formal) model
solution within the formal model
abstraction
specification
interpretation
transformation
Performance
evaluation
Real-world problems & questions
improvement

## Slide 15: Kendall‘s Notation
Single-stage queueing systems

## Slide 16: Single-Stage Queueing Models
Single-stage: Jobs or customers arrive at the queue, get processed, and leave the system.
Queueing model requires the definition of the following components:
  Traffic sources and associated random arrival processes describing the time between arrivals of jobs in the system.
  Service units (or servers) and associated random variables for the duration of service processes.
  Queues and associated waiting room capacity and operating disciplines.
Arrival process
Arrival times
Waiting
space
Service
unit
Departure
times
Processing
time
Waiting
time
Traffic sources

## Slide 17: Kendall‘s Notation
Single-stage queueing models can be described using Kendall’s notation

## Slide 18: Extended Kendall‘s Notation
A/B/n/S/m/D
A – arrival process: interarrival times (IAT); e.g. M for Poisson process
B – service process: processing times; e.g. D for deterministic service times
n – number of servers or service units; e.g. for single server system
S – capacity of waiting queue; e.g. loss system ; e.g. delay system
m – size of customer population; default
D – service discipline, e.g. FIFO (First In – First Out), PS (Processor Sharing)

## Slide 19: Remark: Extended Kendall‘s Notation
Compact notation A/B/n-S
  specifies A, B, n, S,
  assumes and D = FIFO.
  Extended notation is then A/B/n/S/∞/FIFO.
Extended notation: Some textbooks use the total capacity of the system instead of the capacity S of the waiting queue only: A/B/n/S/m/D
Clarification: We refer to the capacity of the waiting queue and use A/B/n/S/m/D or the short notation A/B/n-S.
Example:
  The system with total capacity S+n is written as A/B/n/n+S/m/D.
  The loss system A/B/n implies A/B/n-0 or A/B/n/0/∞/FIFO.
  The delay system A/B/n implies A/B/n-∞ or A/B/n/∞/∞/FIFO.

## Slide 20: Notation for Arrival and Service Processes
GI – General independent
  Arrival processes with renewal properties
  Arrival or service process can be described with a random variable
  Realizations of these random variables are statistically independent of one another
D – Deterministic
M – Markov
  Corresponding random variable follows an exponential distribution
  A M arrival process is a Poisson Process
Ek – Erlang-k distribution
Hk – Hyperexponential distribution (k-th order)

## Slide 21: Modeling Example: Router

## Slide 22: Router Model
packet arrivals
packet departures
(waiting time + processing time)
router
very simplified model
arrival times
departure times
arrival process
arrival times
waiting
space
service
unit
departure times
processing
time
waiting
time
packet departures

## Slide 23: Router Model (f.)
arrival process
arrival times
waiting
space
service
unit
departure times
processing
time
waiting
time
packet departures
very simplified model
Example: M/GI/1 delay system

## Slide 24: Performance Characteristics
Limiting resources
  processing speed of router
Performance measures
  queue length
  throughput: #packets per time
  sojourn / response time = waiting + processing time
  utilization: fraction of time the router is busy (or idle)
Goal of model
  impact of router speed on buffer size (queue length), throughput and utilization
Queueing model
  M/GI/1-∞ delay system
packet arrivals
packet departures
(waiting time + processing time)
router
arrival times
departure times

## Slide 25: Different Delay Systems
Periodic arrivals, identical service times, one server
Periodic arrivals, random service times, one server
5 Min
5 Min
5 Min
5 Min
4 Min
7 Min
4 Min
5 Min
Kendall‘s
notation?
#customers in system
time
#customers in system
time
waiting time

## Slide 26: Modeling Example: Handshaking Protocol

## Slide 27: Handshaking Protocol Illustration

## Slide 28: Traffic Model of the Handshaking Protocol

## Slide 29: Traffic Model of the Handshaking Protocol (f.)

## Slide 30: Handshaking Protocol: Virtual Transmission Time
Assume the following parameters
  constant packet transmission time
  constant singal propagation delay from sender to receiver and back
  packet error probability for any packet
What is the virtual transmission time?

## Slide 31: Handshaking Protocol Summary
Limiting resources
  processing of packets in the system, i.e., sending of packets over the error prone communication channel
Performance measures
  response time of the system (waiting time and virtual transmission time)
  throughput per packet
Goal of model
  impact of packet error probability on performance measures
Queueing model
  GI/GI/1-∞ delay system

## Slide 32: Modeling Example: Network Dimensioning in Mobile Networks

## Slide 33: Network Dimensioning in Mobile Networks
What is the arrival process? What is the service process?

## Slide 34: Summary: Network Dimensioning in Mobile Networks
Limiting resources
  number of communication channels in the mobile cell
Performance measures
  blocking probability of customers’ calls
Goal of model
  dimensioning of the number of required communication channels such that the blocking probability is below a QoS threshold for given parameters
Queueing model
  M/GI/n-0 loss system

## Slide 35: Modeling Example: IoT Load Balancer

## Slide 36: Superposition of Arrival Processes
Kendall’s notation is extended for the superposition of two or more input streams
E.g. two arrival streams, e.g. from sensor 1 and sensor 2 with interarrival times A1 and A2
For 𝑘 independent arrival flows which are described by the same random variable A for the interarrival times
A1+A2/B/n-S
k∙A/B/n-S

## Slide 37: Illustration of Superposition of Arrival Processes

## Slide 38: Example: IoT
Sensors periodically send messages
Deterministic processing time of (small) messages from the sensors
Large number of sensors
How to model the IoT Load Balancer? Kendall’s notation?
  For single sensor ?
  For ?
  For large ?

## Slide 39: Summary: Network Dimensioning in Mobile Networks
Limiting resources
  IoT cloud load balancer
Performance measures
  waiting time or response time of IoT data packets at the load balancer
Goal of model
  dimensioning of the required processing power of the load balancer to keep the
  mean waiting time below a predefined QoS threshold;
  comparison of exact nD/D/1 model with the approximating M/D/1 queue
Queueing model
  nD/1/1 and M/D/1 delay system