## Slide 1
Stochastic Processes
Performance Evaluation of the Internet of Things (IoT)
Module Course: Performance Evaluation of Distributed Systems
Prof. Tobias Hoßfeld, Summer Semester 2022
Chapter 3.1

## Slide 2: Disclaimer and Copyright Notice
Lecture slides, figures, and scripts are based on the open access text book “Performance Modeling and Analysis of Communication Networks”. The book and scripts are licensed under the Creative Commons License Attribution-ShareAlike 4.0 International (CC BY-SA 4.0). If you remix, transform, or build upon the material, you must distribute your contributions under the same license as the original.
The book must be cited and the disclaimer attached when using lectures slides or scripts.
Tran-Gia, P. & Hossfeld, T. (2021). Performance Modeling and Analysis of Communication Networks - A Lecture Note. Würzburg University Press. https://doi.org/10.25972/WUP-978-3-95826-153-2
Website to download book, exercises, slides and scripts: https://modeling.systems/

## Slide 3: Chapter 3
3 Elementary Random Processes
3.1 Stochastic Processes
3.1.1 Definition
3.1.2 Markov Processes
3.1.3 Elementary Processes in Performance Models
3.2 Renewal Processes
3.2.1 Definition
3.2.2 Analysis of Recurrence Time
3.3 Poisson Process
3.3.1 Definition of a Poisson Process
3.3.2 Properties of the Poisson Process
3.3.3 Poisson Arrivals during Arbitrarily Distributed Interval
3.4 Superposition of Independent Renewal Processes
3.4.1 Superposition of Poisson Processes
3.4.2 Palm-Khintchine Theorem
3.5 Markov State Process
3.5.1 Definition of Continuous-Time Markov Chain
3.5.2 Transition Behavior of Markovian State Processes
3.5.3 State Equations and State Probabilities
3.5.4 Examples of Transition Probability Densities
3.5.5 Birth-and-Death Processes

## Slide 4: Stochastic Processes
Examples and definition

## Slide 5: Examples
server
active
idle
random intervals
buffer state of a router
time t
time t
X(t)
X(t)
remaining workload at a server
time t
X(t)

## Slide 6: Objective of Stochastic Modeling
system state
remaining workload at a server
probability density function
state distribution
density

## Slide 7: Stochastic Modeling
Same mean values, but different patterns
discrete uniform distribution X~DU(1,5)
deterministic pattern
value

## Slide 8: Definition
Random points in time
describes process for
  is r.v. at time
Family of random variables
Generalization with family of r.v.s
  index set or parameter set , e.g., time
  state space : collection of all possible values of the r.v.s
Stochastic process: for

## Slide 9: Example: IoT Gateway
is the number of data packets waiting in a device of a computer network
Lecture

## Slide 10: Classification of Stochastic State Processes
continuous state
discrete state
continuous
time
discrete
time

## Slide 11: Markov Processes
Markov property

## Slide 12: Markov Process
Future development can be calculated from current situation
Memoryless process
Definition of Markov Process

## Slide 13: Memorylessness of a Random Variable
Lecture

## Slide 14: Pareto Distribution
Lecture

## Slide 15: Elementary Processes in Performance Models
Arrival process, service process, state process

## Slide 16: Random Processes in Traffic Models
arrival process
service process
state process
traffic source
waiting room

## Slide 17: Characterization of Arrival Process
Interarrival times for -th arrival
Here: are iid. and follow same r.v. (see renewal process)
Remaining time until next arrival
  continuous-time and -state
Arrival process with Markov property
  r.v. is independent of the past
  is iid. for any time instant
  interarrival time A is memoryless
Poisson process is the only single arrival process with Markov property

## Slide 18: Characterization of Service Process
Service time described with r.v. for -th job
Here: service times are iid. for any job and follow r.v.
Several consecutive service times constitute a busy period
Between busy periods there is an idle period
Service process with Markov property
  memoryless service time
  duration until end of operation independent of the past
  exponential distribution is the only continuous distribution with Markov property

## Slide 19: State Process
Depending on traffic model and analysis method, different forms of the state process description are considered
Number of customers
  e.g. for M/GI/1 or GI/M/1
Unfinished work
  e.g. for analysis of GI/GI/1