## Slide 1
Loss System M/M/n
Performance Evaluation of the Internet of Things (IoT)
Module Course: Performance Evaluation of Distributed Systems
Prof. Tobias Hoßfeld, Summer Semester 2022
Chapter 4.1

## Slide 2: Disclaimer and Copyright Notice
Lecture slides, figures, and scripts are based on the open access text book “Performance Modeling and Analysis of Communication Networks”. The book and scripts are licensed under the Creative Commons License Attribution-ShareAlike 4.0 International (CC BY-SA 4.0). If you remix, transform, or build upon the material, you must distribute your contributions under the same license as the original.
The book must be cited and the disclaimer attached when using lectures slides or scripts.
Tran-Gia, P. & Hossfeld, T. (2021). Performance Modeling and Analysis of Communication Networks - A Lecture Note. Würzburg University Press. https://doi.org/10.25972/WUP-978-3-95826-153-2
Website to download book, exercises, slides and scripts: https://modeling.systems/

## Slide 3: Chapter 4
4 Analysis of Markovian Systems
4.1 Loss System M/M/n
4.1.1 Model Structure and Parameters
4.1.2 State Process and State Probabilities
4.1.3 Other System Characteristics
4.1.4 Generalization to Loss System M/GI/n
4.1.5 Modeling Examples and Applications
4.2 Delay System M/M/n
4.2.1 Model Structure and Parameters
4.2.2 State Process and State Probabilities
4.2.3 Other System Characteristics
4.2.4 Delay Distribution
4.2.5 Example: Single Server Delay System
4.3 Loss System with Finite Number of Sources
4.3.1 Model Structure and Parameters
4.3.2 State Process and State Probabilities
4.3.3 Example: Mobile Cell with Finite Number of Sources
4.4 Customer Retrial Model with Finite Number of Sources
4.4.1 Model Structure and Parameters
4.4.2 Recursive Analysis Algorithm
4.4.3 Calculation of Traffic Flows
4.4.4 Example: Mobile Cell with Customer Retrials
4.5 Processor Sharing Model M/M/1-PS

## Slide 4: Model Structure and Parameters

## Slide 5: Loss System M/M/n
Interarrival time A with arrival rate
Service time B with service rate
Offered traffic in pseudo-unit Erlang [Erl]
Pure loss or blocking operation mode
  arriving customer finding all servers occupied upon arrival will be blocked
  blocked customers leave system: no further impact on the system state process

## Slide 6: State Process and State Probabilities
Erlang formula for loss systems

## Slide 7: State Process of M/M/n Loss System
number of customers or busy servers in system at time
Stationary system
Steady-state probabilities (in statistical equilibrium)
x(i) = P(X=i) , i=0,1, ...

## Slide 8: State Transition Diagram
Customer arrival: with rate
  if arriving customer is accepted ()
Customer departure or service termination: with rate
  service time of one of the customers ends ()
(micro) state customers in the system

## Slide 9: Micro State Equations
Rate for leaving state [X = i]
Rate for reaching state [X = i]
Micro state equation for [X = i]
Special cases for [X = 0] and [X = n] and
Normalization condition

## Slide 10: Macro State Equations
Macro state for
Macro state equations

## Slide 11: Macro State Equations: Solution
Lecture
Macro state equations

## Slide 12: Macro State Equations and Erlang Formula for Loss Systems
Macro state for
Macro state equations
Erlang formula for loss systems with offered traffic

## Slide 13: Steady State Distribution
M/M/30-0 with normalized offered load
PASTA property
Blocking probability

## Slide 14: State Probability at Arbitrary and Arrival Times
State probability at arrival time
  arriving customers sees other customers in the system
State probability at arbitrary time
  stationary system is in state at arbitrary time
  time-averaged steady state probability
  analysis of Markov state processes leads to
Due to memoryless property of the Poisson arrival process
  PASTA property: Poisson arrivals see time averages

## Slide 15: Other System Characteristics
Blocking probability (Erlang-B formula), carried traffic, utilization

## Slide 16: System Characteristics
Erlang-B formula
  blocking probability
  PASTA property utilized
Carried traffic
  mean number of occupied servers
  derived using Little’s law and traffic flows
Utilization of a single server
  offered traffic
  normalized offered traffic

## Slide 17: Traffic Flows in M/M/n Loss System
Little’s law
  arrival rate
  mean sojourn time
  mean number of customers

## Slide 18: Generalization to M/GI/n-0
Insensitivity or robustness property

## Slide 19: Insensitivity or Robustness Property
Erlang formula provides steady state probabilities for M/M/n loss system
Generalization to M/GI/n-0
  Erlang formula is also valid for loss systems M/GI/n
  proof in literature, e.g. by Syski
Insensitivity or robustness property
  extends applicability of Erlang formula and Erlang-B formula considerably in practice

## Slide 20: Example: M/GI/1-0
Lecture

## Slide 21: Modeling Examples and Applications
Dimensioning, economy of scale

## Slide 22: Dimensioning of Systems
Trunk size in telephone networks
  best known and earliest application of M/GI/n loss system
  dimension number of trunk groups
GSM cell with n communication channels
  dimension number of channels
DHCP server in ISP environment
  dimension number of IP addresses
Dimensioning means
  finding number of servers such that the
  blocking probability is below a predefined value according to Service Level Agreements (SLAs)

## Slide 23: Numerical Solution: Dimensioning
Efficient implementation of Erlang-B formula: see script “4.1 M/M/n-0 loss system: Erlang-B formula” https://modeling.systems/
a=50 Erl

## Slide 24: Example: GSM Cell
number of channels
call duration with s
arrival rate of Poisson process with
offered load
Goal: Quality of Service (QoS) threshold
Result: channels required

## Slide 25: Economy of Scale
The server utilization increases with number of servers, when we keep required QoS () constant
Larger trunk sizes are more economical
Increase of factor corresponds to the economy of scale.
Increase is limited (flatter shape)

## Slide 26: Economy of Scale in Loss Systems
grouping
System 1
System 2
l1 = l
M
M
1
n
m
pB1
.
.
.
l2 = 2 l
M
M
1
2n
m
pB2
.
.
.
l1 = l
M
M
1
n
m
pB1
.
.
.
Subsystem 1a
Subsystem 1b

## Slide 27: Example: Several Cells
Lecture