## Slide 1
Delay System M/M/n
Performance Evaluation of the Internet of Things (IoT)
Module Course: Performance Evaluation of Distributed Systems
Prof. Tobias Hoßfeld, Summer Semester 2022
Chapter 4.2

## Slide 2: Disclaimer and Copyright Notice
Lecture slides, figures, and scripts are based on the open access text book “Performance Modeling and Analysis of Communication Networks”. The book and scripts are licensed under the Creative Commons License Attribution-ShareAlike 4.0 International (CC BY-SA 4.0). If you remix, transform, or build upon the material, you must distribute your contributions under the same license as the original.
The book must be cited and the disclaimer attached when using lectures slides or scripts.
Tran-Gia, P. & Hossfeld, T. (2021). Performance Modeling and Analysis of Communication Networks - A Lecture Note. Würzburg University Press. https://doi.org/10.25972/WUP-978-3-95826-153-2
Website to download book, exercises, slides and scripts: https://modeling.systems/

## Slide 3: Chapter 4
4 Analysis of Markovian Systems
4.1 Loss System M/M/n
4.1.1 Model Structure and Parameters
4.1.2 State Process and State Probabilities
4.1.3 Other System Characteristics
4.1.4 Generalization to Loss System M/GI/n
4.1.5 Modeling Examples and Applications
4.2 Delay System M/M/n
4.2.1 Model Structure and Parameters
4.2.2 State Process and State Probabilities
4.2.3 Other System Characteristics
4.2.4 Delay Distribution
4.2.5 Example: Single Server Delay System
4.3 Loss System with Finite Number of Sources
4.3.1 Model Structure and Parameters
4.3.2 State Process and State Probabilities
4.3.3 Example: Mobile Cell with Finite Number of Sources
4.4 Customer Retrial Model with Finite Number of Sources
4.4.1 Model Structure and Parameters
4.4.2 Recursive Analysis Algorithm
4.4.3 Calculation of Traffic Flows
4.4.4 Example: Mobile Cell with Customer Retrials
4.5 Processor Sharing Model M/M/1-PS

## Slide 4: Model Structure and Parameters
Stability condition

## Slide 5: Delay System M/M/n
Interarrival time A with arrival rate
Service time B with service rate
Offered traffic in pseudo-unit Erlang [Erl]
Pure delay system
  number of waiting places is assumed to be unlimited
  arriving customer finding upon arrival all servers occupied will join the queue until a server becomes available

## Slide 6: Utilization and Stability Condition
Offered traffic is identical to mean number of occupied servers
Utilization or occupancy of a single server is the mean offered traffic per server
Stability condition
  during single service duration, customers arrive on average
  at most customers can be served during single service duration:
  Stable system requires or

## Slide 7: State Process and State Probabilities

## Slide 8: State Process of M/M/n Delay System

## Slide 9: State Process of M/M/n Delay System
Complete description of stochastic process at time instead of
customers in service
waiting customers
if
î
í
ì
n
=
(t)
X
for
(t)
X
+
(t)
X
0)
=
(t)
(X
n
<
(t)
X
for
(t)
X
=
(t)
X
B
W
B
W
B
B
number of customers in system
steady state probability

## Slide 10: State Transition Diagram
Customer arrival: with rate for (Poisson process)
Customer departure or service termination: with rate
  service time of one of the customers ends ()
  service rate for :
(micro) state customers in the system
all servers occupied

## Slide 11: Macro State Equations
Differentiate macro states
Normalization condition

## Slide 12: Macro State Equations: Solution
Lecture

## Slide 13: Macro State Equations: Solution
Successive iteration yields the solution
Probability of empty system using normalization condition
For stable systems

## Slide 14: Steady State Distribution
Example
  M/M/n delay system for n=10
Geometric tail for
  logarithmic scale: linear for

## Slide 15: Other System Characteristics
Erlang-C formula, waiting probability, mean waiting times

## Slide 16: Waiting Probability
Probability that an arriving customer sees all server busy
Erlang-C formula
Example: M/M/1 delay system

## Slide 17: Waiting Probability: Illustration
Economy of scale in delay systems
  grouping of servers least to lower waiting probabilities for same
  same result for mean waiting times (see later)

## Slide 18: Carried Traffic
Carried traffic is the mean number of occupied servers
Using Little’s theorem
  mean arrival rate in the system:
  mean sojourn time in the system:
  mean number of customers in system:
  Little’s law:

## Slide 19: Mean Queue Length
Mean number of customers in the waiting space
Using waiting probability

## Slide 20: Mean Waiting Time
Mean waiting times of all customers (system I) and of waiting customers (system II)

## Slide 21: Mean Waiting Time of All Customers (System I)
System I (all customers): entire M/M/n system
  mean arrival rate
  mean number of customers in system
  mean sojourn time in system
Little’s law

## Slide 22: Mean Waiting Time of Waiting Customers (System II)
System II (only waiting customers): waiting queue of M/M/n system
  mean arrival rate : arrival rate of waiting customers
  mean number of customers in system : mean queue length
  mean sojourn time in system : mean waiting time of waiting customers
Little’s law

## Slide 23: Mean Waiting Time of Waiting Customers
Near stability boundary , mean waiting time increases sharply
Dimensioning the operation point in lower utilization range

## Slide 24: Delay Distribution
Waiting time distribution

## Slide 25: Waiting Time Distribution for All Customers
Random variable is the waiting time for all customers
Waiting probability is
normalized waiting time
CCDF

## Slide 26: Waiting Time Distribution: Derivation
Lecture

## Slide 27: Waiting Time Distribution: Derivation (f.)
Lecture

## Slide 28: Examples
Waiting time distribution, economy of scale

## Slide 29: Example: Waiting Time Distributions M/M/n
waiting time
CCDF
CCDF
waiting time
CDF
waiting time
CDF
waiting time
linear scale
logarithmic scale
parameter

## Slide 30: Quantiles of Waiting Times
95% Quantile of waiting time

## Slide 31: Economy of Scale for Delay Systems
grouping
System 2
l
2
=
2
l
M
M
1
2n
m
M
2
W
2
p
W
2
.
.
.
l
2
=
2
l
M
M
1
2n
m
M
2
W
2
p
W
2
.
.
.
.
.
.
System 1
l
1
= l
M
M
1
n
m
p
W
1
W
1
.
.
.
l
1
= l
M
M
1
n
m
p
W
1
W
1
.
.
.
Teilsystem 1a
Teilsystem 1b
l
1
= l
M
M
1
n
m
p
W
1
W
1
.
.
.
.
.
.
l
1
= l
M
M
1
n
m
p
W
1
W
1
.
.
.
.
.
.
Subsystem 1a
Subsystem 1b